## Slide 1: Digital Images

## Slide 2: Digital Image
2
1 pixel
a grid of squares, each of which contains a single color
each square is called a pixel (for picture element)
Notes: 2

## Slide 3: Digital Image
3
a grid of squares, each of which contains a single color
each square is called a pixel (for picture element)
Color images have 3 values per pixel; monochrome images have 1 value per pixel.
Notes: 3

## Slide 4: Digital Image
A set of pixels (picture elements, pels)
Pixel means
  pixel coordinate
  pixel value
  or both
Both coordinates and value are discrete

## Slide 5: Example
640 x 480 8-bit image

## Slide 6: DIGITAL IMAGE REPRESENTATION
PIXEL VALUES IN HIGHLIGHTED REGION
CAMERA
DIGITIZER
Samples the analog data and digitizes it.
A set of number in 2D grid

## Slide 7: What is a Digital Image? (cont…)
Common image formats include:
  1 sample per point (B&W or Grayscale)
  3 samples per point (Red, Green, and Blue)
For most of this course we will focus on grey-scale images

## Slide 8: GRAY LEVEL
WE CALL THE INTENSITY OF A MONOCHROME IMAGE f AT COORDINATE (x, y) THE GRAY LEVEL (L) OF THE IMAGE AT THAT POINT.
Thus, l lies in the range
Lmin is positive and Lmax is finite.
Gray scale = [Lmin, Lmax]
Common practice, shift the interval to [0,L] : 0 = black, L-1 = white

## Slide 9: Digital Image Representation
9
Image Size
  Number of bits required to store an image
  Image having 2k intensity levels
    k – bit image
    256 intensity levels – 8 bit image
Notes: 9

## Slide 10: Image Size

## Slide 11: Spatial & Gray Level Resolution

## Slide 12: Spatial Resolution
12
Notes: 12

## Slide 13: Spatial Resolution
13
Notes: 13

## Slide 14: Intensity Level Resolution
14
Intensity level resolution refers to the number of intensity levels used to represent the image
  The more intensity levels used, the finer the level of detail in an image
  Intensity level resolution is usually given in terms of the number of bits used to store each intensity level
Notes: 14

## Slide 15: Intensity Level Resolution
15
Number of Bits
Number of Intensity Levels
Examples
1
2
0, 1
2
4
00, 01, 10, 11
4
16
0000, 0101, 1111
8
256
00110011, 01010101
16
65,536
1010101010101010
Notes: 15

## Slide 16: Intensity Level Resolution
16
Notes: 16

## Slide 17: Intensity Level Resolution
17
128 grey levels (7 bpp)
64 grey levels (6 bpp)
32 grey levels (5 bpp)
16 grey levels (4 bpp)
8 grey levels (3 bpp)
4 grey levels (2 bpp)
2 grey levels (1 bpp)
256 grey levels (8 bits per pixel)
Notes: 17

## Slide 18: Resolution: How much is enough?
18
How many samples and gray levels are required for a good approximation?
  Quality of an image depends on number of pixels and gray-level number
  The more these parameters are increased, the closer the digitized array approximates the original image
  But: Storage & processing requirements increase rapidly as a function of N, M, and k
Notes: 18

## Slide 19: Resolution: How much is enough?
19
Depends on what is in the image and what you would like to do with it
Notes: 19

## Slide 20: Image Resizing
20
Pixel replication
[1 2 3 4 5]
[1 1 2 2 3 3 4 4 5 5] (One step)
[1 1 1 2 2 2 3 3 3 4 4 4 5 5 5] (Two step)
Notes: 20

## Slide 21: Enlarging an Image
21
Example:
zoom this image 4x to get this image.
Start with a blank image 4 times the linear dimensions of the original.
Fill in every 4th pixel in every 4th row with the original pixel values.
.
.
.
Notes: 21

## Slide 22: Enlarging an Image
22
Detail showing every 4th pixel in every 4th row with the original pixel values.
…
…
…
…
…
…
Notes: 22

## Slide 23: Enlarging an Image
23
Replicate the values
Notes: 23

## Slide 24: Image Interpolation
24
Nearest neighbour interpolation
  Simple but produces undesired artefacts
Bilinear Interpolation
  Contribution from 4 neighbors
Bicubic Interpolation
  Contribution from 16 neighbors
Notes: 24

## Slide 25: Interpolation: Comparison
We’ll enlarge this image by a factor of 4 …
… via bilinear interpolation and compare it to a nearest neighbor enlargement.

## Slide 26: Interpolation: Comparison
To better see what happens, we’ll look at the parrot’s eye.
Original Image

## Slide 27: Interpolation: Comparison
Pixel replication
Bilinear interpolation

## Slide 28: Interpolation: Comparison
Pixel replication
Bilinear interpolation